## Slide 1
RTL & DV Fundamentals — Three Designs, One Verification Flow
Sequence Detector · Traffic Light Controller · Synchronous FIFO
Designed, simulated, specified, and verification-planned
Icarus Verilog v12.0 · 6 simulations · 13 logged issues
Nur Mohammad Abdullah — Asmicore Semiconductor Internship
Asmicore Semiconductor · Internship Program · Day 14
Notes: Opening line: "Over 14 days I built three RTL blocks, verified each in Icarus Verilog, wrote a specification and a verification plan for all three, and kept an issue log that includes the mistakes as well as the wins. The RTL turned out to be the easy part — the discipline around it is what this assignment actually taught me."
Set expectations for the shape of the talk: two foundation slides, then one section per design, then the spec-and-verification half, then an honest closing on what is done versus what is only planned.

## Slide 2
OVERVIEW
What I Built, and What Ships With It
Sequence Detector — pure control FSM (overlapping 1011)
Traffic Light — FSM + datapath (timed phases via a down-counter)
Synchronous FIFO — pure datapath (pointers + count)
Per design: RTL → smoke test → regression → spec → features → checkers → coverage
Deliverables: RTL, testbenches, RTL_Specifications.docx, Knowledge Base, Issue Log
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
2 / 18
Notes: The three designs are deliberately ordered: a pure control FSM, then an FSM driving a datapath, then a pure datapath. Each one introduces a new class of correctness concern — state transitions, then timing, then pointer and count bookkeeping — so the bugs I could hit changed shape as I went.
Point at the deliverables line and say the repo has a README that maps every file to the day that produced it, so the evaluator can navigate it without me.

## Slide 3
FOUNDATIONS · STUDY BLOCK 1
What RTL Actually Is — and Why FSMs Dominate Control Logic
RTL sits between behavioural description and gate-level netlist
Flow: RTL → synthesis → place & route → GDSII → fab
HDL describes concurrent structure, not a sequence of instructions
logic is the modern default; always_ff is the only place state changes
Moore = output from state alone · Mealy = output from state and input
Encoding trade-offs: binary (compact) · one-hot (fast decode) · gray (low noise)
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
3 / 18
Notes: The single biggest mental shift coming in was that every assign and every always block is running all the time, simultaneously — the top-to-bottom order in the file means nothing. That reframing is what makes the two-block FSM style obvious rather than arbitrary: one clocked block that does nothing but update the state register, one combinational block that computes next state. Separating them removes a whole class of bugs.
If asked to be concrete about non-synthesisable constructs: #10 delays, initial blocks, $display/$monitor, classes and $random, and ===/!== for X/Z checking — all simulation-only, none of them map to a physical structure.
The Moore/Mealy distinction on this slide is not academic — it is exactly the decision that shaped RTL #1, which is slide 6.

## Slide 4
FOUNDATIONS · STUDY BLOCK 2
Why Verification Is Its Own Discipline
Verification: did we build the design right? · Validation: did we build the right design?
You cannot simulate every input — state-space explosion is why coverage exists
Testbench anatomy: stimulus → DUT → monitor → checker/scoreboard → coverage
Directed tests hit the corners you know; random tests find the ones you didn't
Assertions fire every cycle, automatically — manual checks fire only where you remembered
Cost of a bug grows ~10× at each stage it escapes
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
4 / 18
Notes: The core argument for separating the roles: if the same person designs and verifies a block, their mental model of "what it should do" is baked into both the RTL and the tests, so a misunderstanding of the spec passes both silently. A DV engineer writes the plan from the specification, deliberately not from reading the RTL, so their idea of correct behaviour isn't anchored to whatever the designer happened to build.
Monitor versus scoreboard, since it's a likely question: the monitor observes and translates pin-level activity into transactions but never judges; the scoreboard judges by comparing against a reference model. Keeping them separate means interpretation and judgment can be debugged independently.
This slide is the vocabulary the second half of the talk runs on — feature, Req-ID, checker, coverpoint all come from here.

## Slide 5
RTL #1 · SEQUENCE DETECTOR
Sequence Detector — Overlapping 1011
Serial input din, one bit per cycle; detected pulses once per match
"Overlapping" is the whole point: 1011011 contains two matches sharing the middle 1
Interface: clk, rst_n (async, active-low), din → detected
detected — active-high, exactly one cycle, Moore output
Async reset chosen so the FSM has a known state even before the clock runs
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
5 / 18
Notes: Walk the interface table the way the spec does it — the rule I applied is that a port description must say when the signal is asserted and *what it causes*, not just restate the port's name. So detected isn't "the output flag," it's "pulses HIGH for exactly one cycle when the FSM confirms din has completed an occurrence of 1011, as a pure decode of the current state."
Emphasise overlapping. It is the design's reason to exist, and it is what forced the design decision on the next slide. Non-overlapping would have been a simpler machine and a less interesting assignment.

## Slide 6
RTL #1 · SEQUENCE DETECTOR
Five States, Because Four Would Be Mealy
IDLE — no progress · output 0
S1 — seen 1 · output 0
S10 — seen 10 · output 0
S101 — seen 101, one more 1 completes it · output 0
S1011 — DETECT state, entered from S101 on din=1 · output 1
assign detected = (state == S1011); — a function of state alone
Overlap: S1011 --din=1--> S1 — the trailing 1 seeds the next match
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
6 / 18
Notes: *This is the FSM-explanation checklist item — every state's entry condition and output is on the slide.*
Each state means "the longest suffix of the input seen so far that is also a prefix of 1011." That framing makes every transition derivable rather than memorised.
The key design decision. The Day-2 paper exercise produced a 4-state table, built exactly as the assignment specifies its columns. But in that table detected is HIGH on the row where state is S101 and din is 1 — output depending on state and input, which is Mealy by definition. The Day-4 goal says Moore. A genuine Moore output needs a state that means "just matched," so I added the fifth state.
If asked "did you consider the alternative?" — yes: keep four states and register the combinational condition (state==S101) && din. That reproduces Moore timing and is glitch-free, and I confirmed it produces an identical waveform over 2000 random bits, zero mismatches. But it isn't structurally Moore, because its output is a registered copy of a Mealy condition, not a decode of state. So "which state means detected?" would have no answer. With the 5-state version the answer is S1011, and nothing else. Logged as ISSUE-D2-01.

## Slide 7
RTL #1 · SEQUENCE DETECTOR
When Does detected Fire? — and a Print-Artifact That Fooled Me
Smoke vector 1101011: cycle 7 → S101, detected=0; cycle 8 → S1011, detected=1
One registered cycle after the 4th matching bit — ordinary Moore latency
Corner case — overlap: dedicated self-checking test drives 1011011
Result: two pulses, cycles 5 and 8, a 3-cycle gap (the minimum for 1011)
The smoke vector alone does not test overlap — it contains only one match
ISSUE-D4-01: an early log printed post-edge and looked like zero latency
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
7 / 18
Notes: *Corner-case checklist item, plus a short issue-log story — the long one is slide 9.*
The overlap point first: I noticed the Day-4 smoke vector 1101011 contains only a single 1011, at bits 4–7. So the smoke test could pass without the overlapping behaviour — the design's stated purpose — ever being exercised. That is why there is a separate, self-checking overlap regression that asserts exactly two detections at the expected cycles rather than printing for me to eyeball.
Now the trap. I briefly convinced myself the pulse fired in the same cycle as the 4th bit, because the original log printed post-edge values: on that row the state register had already advanced past S101, so detected=1 sat next to the advanced state and looked simultaneous. The tell was that the state on that row was no longer S101 — which can only be true one edge later. Fixing the log to print pre-edge made the one-cycle latency obvious.
Takeaway, and it recurs on slide 9: **verify how your evidence is sampled before you trust what it appears to show.**

## Slide 8
RTL #2 · TRAFFIC LIGHT
Traffic Light — the FSM Decides What, the Counter Decides How Long
Four phases, fixed round-robin: MAIN_GREEN → MAIN_YELLOW → SIDE_GREEN → SIDE_YELLOW
Durations 4, 2, 6, 2 → a 14-cycle loop; all parameterised
No external input — the only thing that drives a transition is the counter hitting 0
State register + down-counter in one always_ff; next-state, duration lookup, outputs each in their own always_comb
Six light outputs are pure Moore functions of state; safe all-red default
Documented safety rule: the other road stays RED for the whole yellow phase
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
8 / 18
Notes: This is the FSM+datapath pattern the day was built around. A pure FSM can't express "stay here for four cycles" — you'd need four states to say it, which doesn't scale. Splitting it means the case statement is just the fixed sequence and every timing question lives in the counter.
Parameterising the durations is what makes the design testable: real traffic timings would make a simulation impractically long, so small values let a full loop run in 14 cycles. The counter is sized off MAX_DURATION, so raising a duration only requires touching that one parameter.
The yellow-phase rule is a design decision I wrote down rather than left implicit — during both yellow phases the opposing road is red for the entire phase. There is never a cycle where both roads show anything but "one green or yellow, one red." Someone reading the RTL later should never have to guess whether that was intentional.

## Slide 9
RTL #2 · TRAFFIC LIGHT
ISSUE-D5-02 — A Bug That Hid Behind Its Own Test
Symptom: the first MAIN_GREEN lasted 5 cycles; every later one, 4
Cause: reset loaded MAIN_GREEN_TIME (4) instead of MAIN_GREEN_TIME-1 (3)
A D-cycle phase needs the counter to step D-1 … 0 → the reload value is always D-1
Why it was invisible (ISSUE-D5-03): the testbench dropped the reset cycle from its printout
So 5 cycles printed as 4 rows — matching the correct later phase
Fix: load MAIN_GREEN_TIME-1 at reset · and log per-cycle with count exposed
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
9 / 18
Notes: *This is the required issue-log item: one real problem, its cause, and its resolution, told start to finish.*
The off-by-one itself is unremarkable. What makes it worth the slide is that my "run two full loops and compare them" check did not catch it — it hid it. The original testbench deasserted reset then logged inside a for loop of @(negedge clk), so the first logged row landed after the first active clock edge and the reset-loaded cycle was never printed. The buggy 5-cycle first phase printed as 4 rows. The correct 4-cycle later phase also printed as 4 rows. They looked consistent, so the comparison "passed."
Worse — and this is the part that genuinely changed how I think — the same testbench run against the corrected RTL prints only 3 MAIN_GREEN rows, which would look like a failure of a correct design. A mis-sampled printout can both validate a broken design and reject a working one.
The fix was two things: correct the reset load, and rewrite the logging into an always @(posedge clk) block that reads registered values in the cycle they're held, with the internal count exposed as a column so durations are read numerically instead of by counting rows. Only after fixing the test was the bug visible at all.
It is now a named regression, RST_001, so it cannot come back silently.

## Slide 10
RTL #3 · SYNCHRONOUS FIFO
Synchronous FIFO — 8×8, Count-Based
Memory array + wr_ptr + rd_ptr + count, all in one always_ff
full = (count == DEPTH) · empty = (count == 0) — combinational
Why count, not pointer compare: wr_ptr == rd_ptr is true when full and when empty
count width is $clog2(DEPTH+1) = 4 bits (0…8) — one wider than the pointers
Wraparound: wr_ptr <= (wr_ptr == DEPTH-1) ? 0 : wr_ptr + 1
dout is a combinational peek at mem[rd_ptr] — gate on empty before trusting it
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
10 / 18
Notes: The count register is the one design decision that removes the classic full-versus-empty ambiguity. Both conditions genuinely make the pointers equal, so no amount of comparing them can distinguish the two; the alternative standard approach is an extra bit on each pointer, and I chose the count register because it's the simpler of the two and reads directly.
The count-width detail is where a beginner FIFO usually breaks: pointers only need to address 0–7, which is 3 bits, but count must represent 0 through 8 inclusive — nine values — which needs 4. Getting that wrong makes full never assert.
On dout: it's a combinational peek rather than a registered output, which keeps the design to exactly the four registers the assignment specifies. The trade-off is that when empty is high, dout shows stale leftover data. That is not a bug, but it is a contract — any consumer must gate on empty first — so I documented it in the RTL comments, the spec, and the smoke log rather than leaving it as an unstated assumption.

## Slide 11
RTL #3 · SYNCHRONOUS FIFO
FIFO — Handling Every (wr_en, rd_en) Combination
Both enables qualified by !full / !empty before the case statement
→ all four cases 00/01/10/11 then encode the right behaviour automatically
Write while full → blocked (poison 0xFF never reappears in any read)
Read while empty → blocked (no count underflow)
Simultaneous R+W, partially filled → both proceed, count unchanged
Simultaneous while full → read only · while empty → write only
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
11 / 18
Notes: Corner-case checklist item.
The elegance here is that qualifying the enables first means I never had to special-case the tricky combinations — they fall out of the same four-way case. That's worth saying out loud because it's a structural choice, not a lucky one.
A test-plan gap I found and closed (ISSUE-D6-01): the assignment's specified smoke sequence is fill-completely-then-drain-completely, so it never asserts wr_en and rd_en in the same cycle — yet handling simultaneous read+write is separately, explicitly required. Implementing that logic without ever driving a cycle that exercises it means it's written, not verified. So I extended the testbench with three added cycles covering the full, partial, and empty sub-cases. Not an RTL bug — a coverage gap, and the same principle the Day-9 and Day-12 traceability work is built on, in miniature: a requirement with no test behind it isn't confirmed.
The FIFO RTL itself was correct on the first simulation run. Worth being honest that not every design needs a war story.

## Slide 12
VERIFICATION · EVIDENCE
Six Simulations — What Was Actually Run
Detector: smoke (1101011) · self-checking overlap regression (1011011) — 2 pulses ✓
Traffic Light: smoke (20 cycles, full loop + wraparound) · min-duration regression ✓
FIFO: smoke (fill / block / drain / block + simultaneous R/W) · multi-wrap regression ✓
Multi-wrap: 3 fill-drain cycles, 24 writes / 24 reads, checked against a software reference queue — 0 mismatches
All three designs compile clean under iverilog -g2012 -Wall — zero warnings
Every run archived: verbatim log + .vcd + waveform PDF
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
12 / 18
Notes: Two of the six are genuinely self-checking — the overlap test and the multi-wrap test assert their results rather than printing for a human to read. The multi-wrap one is the test I lean on hardest, because it carries a software reference queue: it's the closest thing in this set to a real scoreboard.
Two of these regressions exist because writing the Day-7 corner-case lists made me notice untested assumptions rather than untested code. ISSUE-D7-01: the traffic light's minimum duration of 1 cycle had only ever been reasoned about, never simulated — so I overrode MAIN_YELLOW_TIME to 1 and confirmed the phase occupies exactly one cycle with no skip and no extra hang. ISSUE-D7-02: pointer wraparound had only been exercised once per pointer, and a systematic error at the wrap seam could plausibly hide on a first pass — so I ran three consecutive wraps.
Honest detail worth volunteering: while building the multi-wrap testbench I found a bug in the testbench — inconsistent wait patterns between the write and read tasks that would have silently dropped the last write of every fill phase. I caught it by reasoning through the task sequencing before trusting the result. A testbench bug doesn't announce itself the way a compile error does.

## Slide 13
SPECIFICATION
The Spec as a Contract — Walking One Design's Sections
Overview → Key Features → Interface Table → Microarchitecture
FSM Specification → Timing → Corner Cases → RTL Code
Test of a good spec: could a DV engineer write correct tests without opening the RTL?
Interface rows state when a signal asserts and what it causes — not just its name
Every non-obvious decision is written down (reset load value, yellow-phase rule, stale dout)
Widths, names, and reset values must match the RTL exactly
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
13 / 18
Notes: Spec-walkthrough checklist item — pick the FIFO and walk it live.
Take the FIFO's interface table as the example. full is not "the full flag" — it's "asserts combinationally whenever count == DEPTH, and blocks any write attempted while it is high." A DV engineer can write a test from that sentence. They cannot write one from "the full flag."
The Day-8 re-read pass is worth mentioning here, because it's the part of spec writing that surprised me. Writing a rigorous spec for code that was already "done" surfaced three real inconsistencies that had been sitting unnoticed (ISSUE-D8-01) — a stale timing comment, a comment citing the wrong issue ID, and a leftover template artifact with a missing ` timescale ``. None were logic bugs, but a comment that cross-references the wrong issue quietly misleads the next person who tries to understand why a line is written that way.
The lesson I'd state plainly: a bug that is found but not fixed is almost as bad as one never found, if nothing forces a revisit. Scheduling a deliberate re-read is what caught it.
Known follow-up, stated rather than hidden: the spec document predates the 5-state Moore rewrite and the traffic-light reset fix, and does not yet carry the Day-12 Req-ID tables. Reconciling it is the top remaining task.

## Slide 14
DV THINKING
Feature → Req-ID → Checker → Stimulus → Coverage
Feature — one named, independently testable behaviour (write_blocked_when_full)
Req-ID — a stable handle: RST / FUNC / CORNER / NEG / STRESS, never reused
Checker — assertion (always-true invariant) · scoreboard (data vs reference) · expected-value
Stimulus — directed hits the corner you name; random finds the one you didn't
Coverpoint — the bin that proves the feature was actually exercised
FIFO: Day-3's 5 features → refined to 8, each traced end to end
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
14 / 18
Notes: *DV-concepts checklist item — define feature, Req-ID, checker, coverpoint.*
Granularity is a real skill, not a formality. Day-3's feature 4 bundled two independently testable behaviours — the flag asserting, and a write actually being blocked as a consequence. You can break one without the other, so it split into CORNER_001 and NEG_001.
More significant: there was no empty/read-blocking feature anywhere in the original list. Only the full/write side existed. I found it by deliberately asking "is there a mirror-image feature for every one-sided one?" — a habit worth naming, because that kind of omission is invisible until you go looking for its opposite. Five features became eight (ISSUE-D9-01).
One self-correction I'd volunteer (ISSUE-D10-01): I nearly assigned count_unchanged_on_simultaneous_read_write an expected-value checker, because that's literally how Day 6 happened to test it. That's reasoning from test history instead of from the property. "Count doesn't change when both enables fire" should hold on every cycle regardless of what stimulus produced the condition — that's assertion-shaped. **Checker type follows the nature of the property, not the stimulus that first exposed it.**

## Slide 15
DV THINKING · COVERAGE
FIFO count — Why Five Bins, Not Three
The obvious model: empty / mid / full — three bins
What I used: empty={0} · almost_empty={1} · mid={2..6} · almost_full={7} · full={8}
The two boundary-adjacent bins are deliberate, not padding
Off-by-one bugs hide next to a boundary, not at it
Concrete precedent: ISSUE-D5-02 was exactly that — one step from the boundary
Coverage guidance for datapaths says cover 0, 1, max-1, max — this is why
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
15 / 18
Notes: *Coverage-model checklist item: one coverpoint, explained in depth, and why it matters.*
This is the coverage model I can defend hardest, because the reasoning isn't borrowed. Folding 1 and 7 into a mid bin would mean a test suite could report full coverage of count while never once exercising the value where an off-by-one would actually show. I already got bitten by an off-by-one sitting one step away from a boundary in the traffic light — so treating the adjacent values as their own bins is a direct response to a bug I actually saw in this program, not a textbook precaution I copied.
If asked about the cross: wr_en × rd_en gives four bins — neither, write only, read only, both — and the "both" bin is the one that matters, because it's the case the assignment's own smoke sequence never generates.
Worth flagging one nuance for the traffic light's mutual-exclusion coverage: illegal_both_green = {1,1} is a bin you never want hit. Filling it would be a failure, not progress toward closure. The goal there is confirming the assertion had many opportunities to fire and never did.

## Slide 16
DV THINKING · SELF-AUDIT
Traceability Check — What the FIFO Had That the Others Didn't
Days 9–11's exercises were scoped to the FIFO throughout
Day-12 audit: the Detector and Traffic Light had coverage models and assertions…
…but no Req-IDs, no priorities, no checker assignments, no traceability
12 of 20 features across the three designs were untraced — including 8 P0s
Worst of it: ISSUE-D5-02, a real fixed bug, had no permanent regression test
Closed it: full Feature → Req-ID → Checker → Stimulus → Priority → Coverage tables for all three
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
16 / 18
Notes: This is the most honest slide in the deck, and I'd rather present it than have someone find it.
The audit's real value wasn't tidying up tables. It was discovering that the process I'd built did not automatically generalise. The FIFO got the full treatment across three days because that's what the assignment's exercises name; the other two designs quietly didn't, and nothing would have forced a revisit except deliberately running the check.
The specific consequence is the one worth dwelling on. ISSUE-D5-02 was found, root-caused, fixed, and re-simulated — and then had *nothing in the plan requiring it to be checked again*. It was a one-time fix, not a regression. Now it's RST_001 for the traffic light, with a coverage bin that confirms reset loads MAIN_GREEN_TIME-1, so a future change that reintroduces the bug has a named test whose failure catches it.
That's the difference between fixing a bug and closing it.

## Slide 17
STATUS
What's Verified, and What a DV Engineer Would Do Next
Done: three RTLs simulate correctly · 6 tests (3 smoke + 3 focused regressions)
Done: full written verification plan — features, Req-IDs, checkers, priorities, coverage models
Deliberately not done: none of it is coded as SystemVerilog yet
No covergroup/bins, no assert property (SVA), no scoreboard with a reference model
→ therefore no measured coverage numbers — the plan is a specification
Next: turn every "Coverage Item" cell into real SV and collect actual percentages
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
17 / 18
Notes: I want to be explicit that this is a planning deliverable, not a measured-coverage one. Claiming closure I haven't measured would undercut everything else in the talk — and "high coverage doesn't guarantee correctness, but low coverage guarantees insufficient testing" cuts both ways: unmeasured coverage guarantees nothing at all.
The concrete next step is mechanical and well-defined, which is itself a sign the planning work was worth doing: every row in those tables already names its checker type and its coverage item, so building the real testbench is transcription plus a reference model, not fresh design thinking.
The three smoke tests are directed and read by eye; only two of the six regressions are self-checking. Turning the rest into automated checks would be the first thing I'd do.

## Slide 18
CLOSING
What I'd Emphasise
The RTL was the easy part — the discipline around it was the real content
Two bugs taught the most: a Moore/Mealy timing confusion, and a bug hidden by its own test
Recurring lesson: hand-trace, then simulate — and verify how you're sampling before you trust it
Every failure I hit came from trusting a write-up or a by-eye log over the simulation
Everything is traceable: feature → test → coverage, with an issue log that keeps the unflattering entries
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
18 / 18
Notes: *This section is intentionally a scaffold. Fill in each prompt honestly in your own words before Day 14 — it has to come from the person who did the work, and reading it aloud is a checklist requirement.*
- What I understood well: —
- What was genuinely difficult: —
- The most important thing I learned: —
- One thing I would do differently: —
- One question I still have: —
Close by returning to the through-line: the three designs are correct, but the part I'd defend hardest is the honesty of the record around them — the issue log includes the entries where I was wrong, the coverage model exists because of a bug I actually hit, and the Day-12 audit is on a slide precisely because it found a gap in my own process.
Then open for Q&A. Be ready to jump to slide 6 (the state diagram) and slide 9 (the issue story) — those draw the most questions. Backup slides follow.

## Slide 19
BACKUP · FOR Q&A
Backup — Sequence Detector, All 10 Transition Arcs
IDLE —0→ IDLE (self-loop, no progress) · IDLE —1→ S1
S1 —0→ S10 · S1 —1→ S1 (self-loop, still just …1)
S10 —0→ IDLE (100, no usable prefix) · S10 —1→ S101
S101 —0→ S10 (1010, trailing 10 still useful) · S101 —1→ S1011 (match)
S1011 —0→ S10 · S1011 —1→ S1 (overlap)
Output: detected = 1 in S1011 only; 0 in all other states
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
BACKUP 1
Notes: Backup slide — not presented unless asked. Ten arcs = 5 states × 2 input values, and 100% transition coverage means all ten traversed, including both self-loops.
For an FSM the transition table is the authoritative specification, not the diagram — the diagram is a visual aid, and if they ever disagree the table is what gets implemented.
The overlap arc is the interesting one: for 1011 the only proper suffix that is also a prefix is the trailing 1, which is why S1011 behaves exactly like S1 on the next input.

## Slide 20
BACKUP · FOR Q&A
Backup — 13 Logged Issues, 8 FIFO Features
Design bugs: D5-01 (part-select syntax) · D5-02 (reset off-by-one)
Testbench bugs: D5-03 (mis-sampled logging) · multi-wrap task sequencing
Design decisions resolved: D2-01 (Moore vs Mealy) · D4-01 (pulse timing)
Coverage/plan gaps: D6-01 · D7-01 · D7-02 · D9-01 · D12-01
Self-corrections: D3-01 (terminology) · D10-01 (checker type) · D8-01 (doc consistency)
FIFO features: RST_001 · FUNC_001-002 · CORNER_001-003 · NEG_001-002
RTL & DV Fundamentals — 14-Day Assignment · Nur Mohammad Abdullah
BACKUP 2
Notes: Backup slide. The categorisation is the point: only two entries are genuine RTL bugs. The rest are testbench bugs, design decisions that needed resolving, gaps in the plan rather than the code, and places I corrected my own earlier reasoning.
That distribution is honest and, I think, realistic — most of what goes wrong in verification isn't the design being wrong, it's the process around it having a hole in it.
If asked which single entry I'd point to: ISSUE-D5-03, the testbench that masked a real bug. It's the one that changed how I read evidence.